## Slide 1
Kieran Hitchcock
Anonymous Head Counting in Lecture Theatres

## Slide 2
People counting in crowds has been successfully implemented with colour cameras with accuracy up to 96% in large crowds [1]. However, colour cameras have problems in varying lighting conditions and do not preserve anonymity.
Low resolution thermal cameras do not record any identifying features. However, they are generally used with a top-down view to prevent ‘blob merging’ [2]. The top-down view would not capture large areas such as a lecture theatre.
This project looks to overcome these problems by using a single thermal camera with a front view of a lecture theatre to determine the number of people present.
Background

## Slide 3
Method
Colour Mask
Thresholding (dependant on y-axis)
Dilation
Erosion
Laplacian (Contour Detection)
Contour Area Filtering (dependant on y-axis)
More Thresholding to come!
Missed Detections
False Detections
….

## Slide 4
Conclusion
Currently, this method can detect 44/65 people correctly. However it misses 21 people and falsely detects 8 blobs as people.
Previous studies using low resolution thermal cameras have consistently achieved accuracy of up to 85% in a range of images [1].
Going forward, I will look to threshold the larger blobs to separate out individuals and remove small ‘noise’ blobs to get a more accurate count of people in the current image
For future research, I would look to implement a more robust detection method that could work on a range of different lecture theatres and crowds.